## Slide 1: רשתות תקשורת מחשבים פרק 4 - שכבת הרשת
עמית דביר
amitdv@ariel.ac.il
מעבדת סייבר 56.0.49

## Slide 2: Network Switching

## Slide 4: Virtual circuits
Call setup, teardown for each call before data can flow
Each packet carries VC identifier (not destination host address)
Every router on source-dest path maintains “state” for each passing connection
Link, router resources (bandwidth, buffers) may be allocated to VC (dedicated resources = predictable service)
“source-to-dest path behaves much like telephone circuit”
  performance-wise network actions along source-to-dest path
application
transport
network
data link
physical
1. initiate call
2. incoming call
3. accept call
4. call connected
5. data flow begins
6. receive data
application
transport
network
data link
physical

## Slide 5: Datagram networks
no call setup at network layer
routers: no state about end-to-end connections
      no network-level concept of “connection”
packets forwarded using destination host address
1. send datagrams
application
transport
network
data link
physical
application
transport
network
data link
physical
2. receive datagrams

## Slide 6: IP Datagrams on Virtual Circuits
Challenge – when to setup connections
      At bootup time – permanent virtual circuits (PVC)
        Large number of circuits
      For every packet transmission
        Connection setup is expensive
      For every connection
        What is a connection?
        How to route connectionless traffic?

## Slide 7: Source Routing
List entire path in packet
      Driving directions (north 3 hops, east, etc..)
Router processing
      Examine first step in directions
      Strip first step from packet
      Forward to step just stripped off
Receiver
Packet
R2, R3, R
Sender
2
3
4
1
2
3
4
1
2
3
4
1
R2
R3
R1
R3, R
R

## Slide 8: תרגיל
אילו סוגים של רשתות אתם מכירים
Packet switching
Circuit Switching
Virtual Circuit
Source Routing
Global Addresses
Header Size
Router Table Size
Forward Overhead
Virtual Circuits
Setup Overhead
Error Recovery

## Slide 9: Summary
Source Routing
Global Addresses
Header Size
Worst
OK – Large address
Router Table Size
None
Number of hosts (prefixes)
Forward Overhead
Best
Prefix matching
Virtual Circuits
Best
Number of circuits
Pretty Good
Setup Overhead
None
None
Error Recovery
Tell all hosts
Tell all routers
Connection Setup
Tell all routers and Tear down circuit and re-route
Notes: Run: route PRINT or netstat –rn and see the routing table.
Default route, default gateway
Direct delivery to the LAN-located computer and sending to the gateway for all other cases

## Slide 10: DHCP

## Slide 11: IP addresses: how to get one?
Q: How does host get IP address?
1. hard-coded by system admin in a file
2. DHCP: Dynamic Host Configuration
Protocol: dynamically get address from a
server

## Slide 12: DHCP: Dynamic Host Configuration Protocol
Goal: allow host to dynamically obtain its IP address from network server when it joins network
Can renew its lease on address in use
Allows reuse of addresses (only hold address while connected an “on”
Support for mobile users who want to join network

## Slide 13: DHCP overview
  Discover: Host broadcasts “DHCP
  discover” msg
  Offer: DHCP server responds with “DHCP
  offer” msg
  Request: host requests IP address:
  “DHCP request” msg
  Acknowledge: DHCP server sends
  address: “DHCP ack” msg

## Slide 14: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 15: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs

## Slide 16: Soft State: Refresh or Forget
Why is a lease time necessary?
  Client can release the IP address (DHCP RELEASE)
      E.g., “ipconfig /release” at the DOS prompt
      E.g., clean shutdown of the computer
  But, the host might not release the address
      E.g., the host crashes (blue screen of death!)
      E.g., buggy client software
  And you don’t want the address to be allocated forever
Performance trade-offs
  Short lease time: returns inactive addresses quickly
  Long lease time: avoids overhead of frequent renewals

## Slide 17: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 18: DHCP: example
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 19: DHCP: example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DSN server, IP address of its first-hop router

## Slide 20: DHCP: Wireshark output (home LAN)
Message type: Boot Reply (2)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK
Option: (t=54,l=4) Server Identifier = 192.168.1.1
Option: (t=1,l=4) Subnet Mask = 255.255.255.0
Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092;
IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
reply
Message type: Boot Request (1)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A;
Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101
Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name
3 = Router; 6 = Domain Name Server
44 = NetBIOS over TCP/IP Name Server
……
request

## Slide 21: DHCP: Wireshark output (home LAN)

## Slide 22: תרגיל
מה אפשרויות למחשב לקבל IP?
תצורה סטאטית - הגדרות המחשב
תצורה דינמית – DHCP
2) למה אנחנו צריכים שרת DHCP?
מישהו צריך לרכז מי קיבל מה
מה היתרון של ארבעת ההודעות
האפשרות שמספר שרתים יענו לי ובכך השרתים ידעו איזה כתובת לקחתי
מה קורה כאשר יש לנו רשת עם נתבים, האם יש צורך בשרת תחת כל subnet
לא

## Slide 23: Computer Networks IP: Internet Protocol
Notes: הגעתי

## Slide 24: IP Addressing
IP address: 32-bit identifier
interface: connection between host/router and physical link
router’s typically have multiple interfaces
host typically has one interface
IP addresses associated with each interface

## Slide 25: IP Addressing
IP address:
  subnet part (high order bits)
  host part (low order bits)
What’s a subnet ?
  device interfaces with same subnet part of IP address can physically reach each other without intervening router

## Slide 26: Subnets
To determine the subnets, detach each interface from its host or router, creating islands of isolated networks.
Each isolated network is called a subnet.
Subnet mask: number of leftmost bits in IP addresses that define the subnet address

## Slide 27: IP addressing: CIDR
CIDR: Classless InterDomain Routing
subnet portion of address of arbitrary length
address format: a.b.c.d/x, where x is # bits in subnet portion of address

## Slide 28: CIDR Illustration
Provider is given 201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider

## Slide 29: CIDR Implications
Longest prefix match!!
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23 or Provider 2 address
Provider 1
Provider 2
201.10.6.0/23

## Slide 30: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
hierarchical addressing allows efficient advertisement of routing
information:

## Slide 31: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 33: Router

## Slide 34: Generic Router Architecture
Lookup
IP Address
Update
Header
Header Processing
Data
Hdr
Data
Hdr
1M prefixes
Off-chip DRAM
Address
Table
IP Address
Next Hop
Queue
Packet
Buffer
Memory
1M packets
Off-chip DRAM

## Slide 35: What a Router Chassis Looks Like
Cisco CRS-1
Juniper M320
6ft
19”
2ft
Capacity: 1.2Tb/s Power: 10.4kW Weight: 0.5 Ton Cost: $500k
3ft
2ft
17”
Capacity: 320 Gb/s Power: 3.1kW

## Slide 36: IP Lookups find Longest Prefixes
128.9.16.0/21
128.9.172.0/21
128.9.176.0/24
0
232-1
128.9.0.0/16
142.12.0.0/19
65.0.0.0/8
128.9.16.14
Routing lookup: Find the longest matching prefix (aka the most specific route) among all prefixes that match the destination address.

## Slide 37: IP Address Lookup: Binary Tries
Example Prefixes:
a) 00001
b) 00010
c) 00011
d) 001
e) 0101
f) 011
g) 100
h) 1010
i) 1100
j) 11110000
e
f
g
h
i
j
0
1
a
b
c
d

## Slide 38: Address aggregation

## Slide 39: Longest mask matching

## Slide 40: The Internet Network layer
Host, router network layer functions:

## Slide 41: Where are we ?

## Slide 42: IP datagram format

## Slide 44
Notes: להסביר שבממוצע בגלל ה-TCP options זה גדל ל-40

## Slide 45: IPv4 Header Fields
Version: IP Version
  4 for IPv4
HLen: Header Length
  32-bit words (typically 5)
TOS: Type of Service
  Priority information
Length: Packet Length
  Bytes (including header)
Header format can change with versions
  First byte identifies version
Length field limits packets to 65,535 bytes
  In practice, break into much smaller packets for network performance considerations
0
4
8
12
16
19
24
28
31
ver-
sion
HLen
TOS
Length
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source Address
Destination Address
Options (if any)
Data

## Slide 46: IPv4 Header Fields
Identifier, flags, fragment offset  used primarily for fragmentation
Time to live
  Must be decremented at each router
  Packets with TTL=0 are thrown away
  Ensure packets exit the network
Protocol
  Demultiplexing to higher layer protocols
  TCP = 6, ICMP = 1, UDP = 17…
Header checksum
  Ensures some degree of header integrity
  Relatively weak – 16 bit
Options
  E.g. Source routing, record route, etc.
  Performance issues
    Poorly supported
0
4
8
12
16
19
24
28
31
ver-
sion
HLen
TOS
Length
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source Address
Destination Address
Options (if any)
Data

## Slide 47: IPv4 Header Fields
Source Address
  32-bit IP address of sender
Destination Address
  32-bit IP address of destination
Like the addresses on an envelope
Globally unique identification of sender & receiver
0
4
8
12
16
19
24
28
31
ver-
sion
HLen
TOS
Length
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source Address
Destination Address
Options (if any)
Data

## Slide 48: תרגיל
מה משמעות שדה ה-TTL
למרות שהוא מוגדר כ-Time to leave, מדובר על כמות הנתבים שמותר לחבילה לעבור בדרך
2) מדוע יש שדה ID למרות שב-TCP יש seqNum
כל שכבה עומדת בפני עצמה, לדוגמא מה יקרה אם בשכבת התעבורה יעבוד UDP

## Slide 49: IP Fragmentation and Reassembly
Network links have MTU (max. transfer size)
– largest possible link-level frame.
Different link types, different MTUs
Ethernet: 1500 bytes
Some WANs: 576 bytes
Large IP datagram divided (“fragmented”)
within net
One datagram becomes several datagrams
“reassembled” only at final destination
IP header bits used to identify, order related
fragments

## Slide 50: IP Fragmentation and Reassembly
Notes: אריאל ערב

## Slide 51: IP Fragmentation Example #1
host
router
MTU = 4000
IP
Header
IP
Data
Length = 3820, M=0

## Slide 52: IP Fragmentation Example #2
router
router
MTU = 2000
IP
Header
IP
Data
Length = 3820, M=0
3800 bytes
IP
Header
IP
Data
Length = 2000, M=1, Offset = 0
1980 bytes
IP
Data
IP
Header
Length = 1840, M=0, Offset = 1980
1820 bytes

## Slide 53: IP Fragmentation Example #3
IP
Header
IP
Data
Length = 2000, M=1, Offset = 0
1980 bytes
IP
Data
IP
Header
Length = 1840, M=0, Offset = 1980
1820 bytes
host
router
MTU = 1500
IP
Header
IP
Data
Length = 1500, M=1, Offset = 0
1480 bytes
IP
Header
IP
Data
Length = 520, M=1, Offset = 1480
500 bytes
IP
Header
IP
Data
Length = 1500, M=1, Offset = 1980
1480 bytes
IP
Header
IP
Data
Length = 360, M=0, Offset = 3460
340 bytes

## Slide 54: IP Reassembly
Fragments might arrive out-of-order
  Don’t know how much memory required until receive final fragment
Some fragments may be duplicated
  Keep only one copy
Some fragments may never arrive
  After a while, give up entire process
IP
Header
IP
Data
Length = 1500, M=1, Offset = 0
IP
Header
IP
Data
Length = 520, M=1, Offset = 1480
IP
Header
IP
Data
Length = 1500, M=1, Offset = 1980
IP
Header
IP
Data
Length = 360, M=0, Offset = 3460
IP
Data
IP
Data
IP
Data
IP
Data

## Slide 55: Fragmentation Concepts
Highlights many key Internet characteristics
  Decentralized and heterogeneous
    Each network may choose its own MTU
  Connectionless datagram protocol
    Each fragment contains full routing information
    Fragments can travel independently, on different paths
  Best effort network
    Routers/receiver may silently drop fragments
    No requirement to alert the sender
  Most work is done at the endpoints
    i.e. reassembly

## Slide 56: Fragmentation in Reality
Fragmentation is expensive
  Memory and CPU overhead for datagram reconstruction
  Want to avoid fragmentation if possible
MTU discovery protocol
  Send a packet with “don’t fragment” bit set
  Keep decreasing message length until one arrives
  May get “can’t fragment” error from a router, which will explicitly state the supported MTU
Router handling of fragments
  Fast, specialized hardware handles the common case
  Dedicated, general purpose CPU just for handling fragments

## Slide 58: ICMP

## Slide 59: ICMP: internet control message protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header
Notes: לתת דגש על הנושא למרות שיש קצת שקפים

## Slide 60: Overview
IP deficiencies: Lack of error control and assistance mechanisms
The Internet Control Message Protocol (ICMP) is a helper protocol that supports IP with facility for
  Error reporting
  Simple queries

## Slide 61: ERROR REPORTING
ICMP does not correct errors, it simply reports them.
ICMP always reports error messages to the original source.
No ICMP error message will be generated in response to a datagram carrying an ICMP error message.
Checksum: Calculated over entire ICMP message

## Slide 62: Position of ICMP in the network layer & encapsulation

## Slide 63: Frequent ICMP Error message
Type | Code | Description | 
3 | 0–15 | Destination unreachable | Notification that an IP datagram could not be forwarded and was dropped. The code field contains an explanation.
4 | 0 | Source Quench | Notification that an IP datagram has been discarded due to congestion in a router or the dest. host. The source must slow down the sending of datagrams until the congestion is relieved
5 | 0–3 | Redirect | Informs about an alternative route for the datagram and should result in a routing table update. The code field explains the reason for the route change.
11 | 0, 1 | Time exceeded | Sent when the TTL field has reached zero (Code 0) or when there is a timeout for the reassembly of segments (Code 1)
12 | 0, 1 | Parameter problem | Sent when the IP header is invalid (Code 0) or when an IP header option is missing (Code 1)

## Slide 64: Some subtypes of the “Destination Unreachable”
Code | Description | Reason for Sending
0 | Network Unreachable | No routing table entry is available for the destination network.
1 | Host Unreachable | Destination host should be directly reachable, but does not respond to ARP Requests or due to hardware failure.
2 | Protocol Unreachable | The protocol in the protocol field of the IP header is not supported at the destination.
3 | Port Unreachable | The transport protocol at the destination host cannot pass the datagram to an application.
4 | Fragmentation Needed and DF Bit Set | IP datagram must be fragmented, but the DF bit in the IP header is set.

## Slide 65: Timestamp-request and timestamp-reply message format
A system (host or router) asks another system for the current time.
Time is measured in milliseconds after midnight UTC (Universal Coordinated Time) of the current day
Sender fills orig. timestamp by its clocks at depart. Time and sends a request. Receiver responds with reply

## Slide 66: Timestamp (cont’d)
When request arrive, receiver copies orig. Tstp into the reply, fills the receive Tstp by its clocks when time request received. And fills transmit Tstp with time reply departs.
  Sending Time = rx Tstp – orig Tstp
  Receiving Time = returned time – transmit Tstp
  Round-trip time(RTT) = sending time + receiving time
Timestamp-request and timestamp-reply messages can be used to calculate the round-trip time between a source and a destination machine even if their clocks are not synchronized.
The timestamp-request and timestamp-reply messages can be used to synchronize two clocks in two machines if the exact one-way time duration is known.

## Slide 67: DEBUGGING TOOLS
PING : find if a host or router is alive and running
TRACEROUTE : trace the route of a packet

## Slide 68: Ping
Uses ICMP echo request/reply
Source sends ICMP echo request message to the destination address - Echo request packet contains sequence number and timestamp
Destination replies with an ICMP echo reply message containing the data in the original echo request message - Source can calculate round trip time (RTT) of packets
If no echo reply comes back then the destination is unreachable
R1
R2
R3
A
B
Time
Echo request
Echo reply

## Slide 69: Ping example

## Slide 70: ICMP - Example (ping)

## Slide 71: Traceroute
Traceroute records the route that packets take
A clever use of the TTL field
When a router receives a packet, it decrements TTL
If TTL=0, it sends an ICMP time exceeded message back to the sender
To determine the route, progressively increase TTL
  Every time an ICMP time exceeded message is received, record the sender’s (router’s) address
  Repeat until the destination host is reached or an error message occurs

## Slide 72: Traceroute and ICMP
source sends series of UDP segments to dest
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number
when nth set of datagrams arrives to nth router:
  router discards datagrams
  and sends source ICMP messages (type 11, code 0)
  ICMP messages includes name of router & IP address
when ICMP messages arrives, source records RTTs
stopping criteria:
                UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes

## Slide 73: Traceroute (cont’d)
R1
R2
R3
A
B
TTL=1, Dest = B,
port = invalid
TTL=2, Dest = B
TTL=3, Dest = B
TTL=4, Dest = B
Te (R1)
Te (R2)
Te (R3)
Pu (B)
Time
Te = Time exceeded
Pu = Port unreachable

## Slide 79: NAT

## Slide 80: Private Network Accessing Public Internet
Don’t have enough IP addresses for every host in organization
Security
      Don’t want every machine in organization known to outside world
      Want to control or monitor traffic in / out of organization
Internet
Corporation X
W
W
W
S
NAT
W: Workstation
S: Server Machine

## Slide 81: Reducing IP Addresses
Most machines within organization are used by individuals
      “Workstations”
      For most applications, act as clients
Small number of machines act as servers for entire organization
      E.g., mail server
      All traffic to outside passes through firewall
  (Most) machines within organization don’t need actual IP addresses!
Internet
Corporation X
W
W
W
S
NAT
W: Workstation
S: Server Machine

## Slide 82: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers

## Slide 83: NAT: Network Address Translation
Motivation: local network uses just one IP address as far as outside world is concerned:
  Range of addresses not needed from ISP: just one IP address for all devices
  Can change addresses of devices in local network without notifying outside world
  Can change ISP without changing addresses of devices in local network
  Devices inside local net not explicitly addressable, visible by outside world (a security plus).

## Slide 84: NAT: Network Address Translation
Implementation: NAT router must:
outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
. . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr.
remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 85: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 86: NAT traversal problem
client wants to connect to server with address 10.0.0.1
  server address 10.0.0.1 local to LAN (client can’t use it as destination addr)
  only one externally visible NATed address: 138.76.29.7
solution1: statically configure NAT to forward incoming connection requests at given port to server
  e.g., (123.76.29.7, port 2500) always forwarded to 10.0.0.1 port 25000
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
client
?

## Slide 87: NAT traversal problem
Solution 2: Universal Plug and Play (UPnP) Internet Gateway Device (IGD) Protocol. Allows NATed host to:
  learn public IP address (138.76.29.7)
  add/remove port mappings (with lease times)
  i.e., automate static NAT port map configuration
10.0.0.1
NAT
router
IGD

## Slide 88: NAT traversal problem
solution 3: relaying (used in Skype)
      NATed client establishes connection to relay
      external client connects to relay
      relay bridges packets between to connections
138.76.29.7
client
1. connection to
relay initiated
by NATed host
2. connection to
relay initiated
by client
3. relaying
established
NAT
router
10.0.0.1
Notes: להדגיש שנתב NAT מבצע חיבור של חבילות במצב של fregmentation
זה עקב כך שברוב מקרים ה-data שמכיל את ה-transport header נמצא בתת סגמנט הראשון ולכן צריך לאחד שם

## Slide 89
Notes: יש פה טעות במספר זה 3489
Full Cone: A full cone NAT is one where all requests from the same internal IP address and port are mapped to the same external IP address and port. Furthermore, any external host can send a packet to the internal host, by sending a packet to the mapped external address.
Restricted Cone: A restricted cone NAT is one where all requests from the same internal IP address and port are mapped to the same external IP address and port. Unlike a full cone NAT, an external host (with IP address X) can send a packet to the internal host only if the internal host had previously sent a packet to IP address X.
Port Restricted Cone: A port restricted cone NAT is like a restricted cone NAT, but the restriction includes port numbers. Specifically, an external host can send a packet, with source IP address X and source port P, to the internal host only if the internal host had previously sent a packet to IP address X and port P.
Symmetric: A symmetric NAT is one where all requests from the same internal IP address and port, to a specific destination IP address and port, are mapped to the same external IP address and port. If the same host sends a packet with the same source address and port, but to a different destination, a different mapping is used. Furthermore, only the external host that receives a packet can send a UDP packet back to the internal host.

## Slide 91: NAT Considerations
NAT has to be consistent during a session.
      Set up mapping at the beginning of a session and maintain it during the session
          Recall 2nd level goal 1 of Internet: Continue despite loss of networks or gateways
      What happens if your NAT reboots?
      Recycle the mapping that the end of the session
      May be hard to detect
NAT only works for certain applications.
      Some applications (e.g. ftp) pass IP information in payload
      Need application level gateways to do a matching translation
      Breaks a lot of applications.
      Example: Let’s look at FTP
NAT is loved and hated
      - Breaks many apps (FTP)
      - Inhibits deployment of new applications like p2p (but so do firewalls!)
      + Little NAT boxes make home networking simple.
      + Saves addresses. Makes allocation simple.

## Slide 92: IPv6

## Slide 93: IP Address Utilization (‘06)
http://xkcd.com/195/

## Slide 95: What Now?

## Slide 96: IPv6: motivation
initial motivation: 32-bit address space soon to be completely allocated.
additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 98: IPv6 datagram format
priority: identify priority among datagrams in flow
flow Label: identify datagrams in same “flow.”
(concept of“flow” not well defined).
next header: identify upper layer protocol for data
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits

## Slide 99: Next header

## Slide 101: IPv6 Header Cleanup
Different options handling
IPv4 options: Variable length header field. 32 different options.
  Rarely used
  No development / many hosts/routers do not support
    Worse than useless: Packets w/options often even get dropped!
  Processed in “slow path”.
IPv6 options: “Next header” pointer
  Combines “protocol” and “options” handling
    Next header: “TCP”, “UDP”, etc.
  Extensions header: Chained together
  Makes it easy to implement host-based options
  One value “hop-by-hop” examined by intermediate routers
    Things like “source route” implemented only at intermediate hops

## Slide 102: IPv6 Header Cleanup
No checksum
Why checksum just the IP header?
  Efficiency: If packet corrupted at hop 1, don’t waste b/w transmitting on hops 2..N.
  Useful when corruption frequent, b/w expensive
  Today: Corruption rare, b/w cheap

## Slide 103: IPv6 Fragmentation Cleanup
IPv4:
IPv6:
  Discard packets, send ICMP “Packet Too Big”
    Similar to IPv4 “Don’t Fragment” bit handling
  Sender must support Path MTU discovery
    Receive “Packet too Big” messages and send smaller packets
  Increased minimum packet size
    Link must support 1280 bytes;
    1500 bytes if link supports variable sizes
Reduced packet processing and network complexity.
Increased MTU a boon to application writers
Hosts can still fragment - using fragmentation header. Routers don’t deal with it any more.
Large MTU
Small MTU
Router must fragment

## Slide 104: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields

## Slide 105: Tunneling
physical view:
IPv4
IPv4
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6

## Slide 106: Tunneling
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4
IPv4

## Slide 108: Important Concepts
Base-level protocol (IP) provides minimal service level
  Allows highly decentralized implementation
  Each step involves determining next hop
  Most of the work at the endpoints
ICMP provides low-level error reporting
IP forwarding  global addressing, alternatives, lookup tables
IP addressing  hierarchical, CIDR
IP service  best effort, simplicity of routers
IP packets  header fields, fragmentation, ICMP

## Slide 109: 6to4 Basics
Problem: you’ve been assigned an IPv4 address, but you want an IPv6 address
  Your ISP can’t or won’t give you an IPv6 address
  You can’t just arbitrarily choose an IPv6 address
Solution: construct a 6to4 address
  6to4 addresses always start with 2002::
  Embed the 32-bit IPv4 inside the 128-bit IPv6 address
20 02:
207.
CF 2E:
46.
C0 00:
192.
0000
0
IPv4:
IPv6:

## Slide 110: Routing from 6to4 to 6to4
IPv4
Internet
Dest: 16.79.8.0
How does a host using 6to4 send a packet to another host using 6to4?
IPv4 – 207.46.192.0
IPv6 – 2002:CF2E:C000::
IPv4 – 16.79.8.0
IPv6 – 2002:104F:0800::
Dest: 2002:104F:0800::

## Slide 111: Routing from 6to4 to Native IPv6
IPv4 – 192.88.99.1
IPv6 – 2002:: /16
IPv4
Internet
IPv6
Internet
Dest: 192. 88.99.1
IPv4 – 207.46.192.0
IPv6 – 2002:CF2E:C000::
IPv6 – 1893:92:13:99::
Dest: 1893:92:13:99::
Special, anycasted IPv4 address for
6to4 Relay Routers
Many ISPs provide 6to4 relay routers

## Slide 112: Routing from Native IPv6 to 6to4
IPv4 – 192.88.99.1
IPv6 – 2002:: /16
IPv4
Internet
IPv6
Internet
Dest: 207.46.192.0
IPv4 – 207.46.192.0
IPv6 – 2002:CF2E:C000::
IPv6 – 1893:92:13:99::
Dest: 2002:CF2E:C000::
Use normal IPv6 routing to reach a 6to4 relay router

## Slide 113: IPv6 Scope and Multicasting
IPv6 128-bit space is spitted to 64-bit network part and 64-bit host part.
IANA allocates 48-bit networks leaving 64-48 = 16 bit for local subnetting.
IPv6 Address Scope: local, global, etc. scope.
Local scope address – an automatically generated LAN-only valid IPv6 address based on MAC.
There are 8 scopes for multi-casting addresses:
- No formal broadcasting - instead a local network scope
multi-casting.
- Major improvements of multi-casting. Hopefully, it will
be supported broadly and IP (IPv6) multicasting to
become a reality.

## Slide 114: Problems with 6to4
Uniformity
  Not all ISPs have deployed 6to4 relays
Quality of service
  Third-party 6to4 relays are available
  …but, they may be overloaded or unreliable
Reachability
  6to4 doesn’t work if you are behind a NAT
Possible solutions
  IPv6 Rapid Deployment (6rd)
    Each ISP sets up relays for its customers
    Does not leverage the 2002:: address space
  Teredo
    Tunnels IPv6 packets through UDP/IPv4 tunnels
    Can tunnel through NATs, but requires special relays

## Slide 115: Consequences of IPv6
Beware unintended consequences of IPv6
Example: IP blacklists
  Currently, blacklists track IPs of spammers/bots
  Few IPv4 addresses mean list sizes are reasonable
  Hard for spammers/bots to acquire new IPs
Blacklists will not work with IPv6
  Address space is enormous
  Acquiring new IP addresses is trivial
Notes: יאללה kahoot

## Slide 116: Routing Algorithms
Notes: אריאל בוקר/ערב

## Slide 117: IP Forwarding
The Story So Far…
  IP addresses are structured to reflect Internet structure
  IP packet headers carry these addresses
  When Packet Arrives at Router
    Examine header to determine intended destination
    Look up in table to determine next hop in path
    Send packet out appropriate port
How to generate the forwarding table
Router

## Slide 118: Interplay between routing, forwarding
1
2
3
IP destination address in
arriving packet’s header
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
routing algorithm determines
end-end-path through network
forwarding table determines
local forwarding at this router

## Slide 119: Graph Model
Represent each router as node
Direct link between routers represented by edge
  Symmetric links  undirected graph
Edge “cost” c(x,y) denotes measure of difficulty of using link
  delay, $ cost, or congestion level
Task
  Determine least cost path from every node to every other node
    Path cost d(x,y) = sum of link costs
A
E
F
C
D
B
2
3
6
4
1
1
1
3

## Slide 120: Routes from Node A
Properties
  Some set of shortest paths forms tree
    Shortest path spanning tree
  Solution not unique
    E.g., A-E-F-C-D also has cost 7
A
E
F
C
D
B
2
3
6
4
1
1
1
3
Forwarding Table for A |  | 
Dest | Cost | Next Hop
A | 0 | A
B | 4 | B
C | 6 | E
D | 7 | B
E | 2 | E
F | 5 | E

## Slide 121: Ways to Compute Shortest Paths
Centralized
  Collect graph structure in one place
  Use standard graph algorithm
  Disseminate routing tables
Link-state
  Every node collects complete graph structure
  Each computes shortest paths from it
  Each generates own routing table
Distance-vector
  No one has copy of graph
  Nodes construct their own tables iteratively
  Each sends information about its table to neighbors

## Slide 122: Link State

## Slide 123: A Link-State Routing Algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (‘source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k dest.’s
notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current value of cost of path from source to dest. v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path definitively known

## Slide 124: Dijsktra’s Algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'

## Slide 125
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Dijkstra’s algorithm: example
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
notes:
construct shortest path tree by tracing predecessor nodes
ties can exist (can be broken arbitrarily)
uwxvyz

## Slide 126: Dijkstra’s Algorithm: Concept
Node Sets
  Done
    Already have least cost path to it
  Horizon:
    Reachable in 1 hop from node in Done
  Unseen:
    Cannot reach directly from node in Done
Label
  d(v) = path cost from s to v
Path
  Keep track of last link in path
A
E
F
C
D
B
2
3
6
3
1
1
2
3
Source
Node
Done
Horizon
Unseen
0
2
5
3


Current Path Costs

## Slide 127: Dijkstra’s Algorithm: Initially
No nodes done
Source in horizon
A
E
F
C
D
B
2
3
6
3
1
1
2
3
Source
Node
Done
Horizon
Unseen
0





Current Path Costs

## Slide 128: Dijkstra’s Algorithm: Initially
d(v) to node A shown in red
  Only consider links from done nodes
A
E
F
C
D
B
2
3
6
3
1
1
2
3
Source
Node
Done
Horizon
Unseen
0
2
6
3


Current Path Costs

## Slide 129: Dijkstra’s Algorithm
Select node v in horizon with minimum d(v)
Add link used to add node to shortest path tree
Update d(v) information
A
E
F
C
D
B
2
3
6
3
1
1
2
3
Source
Node
Done
Horizon
Unseen
0
2
3


Current Path Costs
6
5

## Slide 130: Dijkstra’s Algorithm
Repeat…
A
C
2
3
6
3
1
1
2
3
Source
Node
Done
Horizon
Unseen
0
2
5
3


Current Path Costs
F
B
D
E

## Slide 131: Dijkstra’s Algorithm
Update d(v) values
  Can cause addition of new nodes to horizon
2
6
3
1
1
2
3
Source
Node
Done
Horizon
Unseen
0
2
4
3

6
Current Path Costs
A
C
3
D
B
E
F

## Slide 132: Dijkstra’s Algorithm
Final tree shown in green
2
6
3
1
1
2
3
Source
Node
0
2
4
3
5
6
A
C
3
D
B
E
F

## Slide 133: Distance Vector

## Slide 134: Distance vector algorithm
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y
then
dx(y) = min {c(x,v) + dv(y) }
v
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y

## Slide 135: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
node achieving minimum is next
hop in shortest path, used in forwarding table
B-F equation says:

## Slide 136: Distance vector algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors’ distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]

## Slide 137: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)

## Slide 138: Distance vector algorithm
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
each node:

## Slide 139: Start
A
E
F
C
D
B
2
3
6
4
1
1
1
3
Table for A |  | 
Dst | Cst | Hop
A | 0 | A
B | 4 | B
C |  | –
D |  | –
E | 2 | E
F | 6 | F
Table for B |  | 
Dst | Cst | Hop
A | 4 | A
B | 0 | B
C |  | –
D | 3 | D
E |  | –
F | 1 | F
Table for C |  | 
Dst | Cst | Hop
A |  | –
B |  | –
C | 0 | C
D | 1 | D
E |  | –
F | 1 | F
Table for D |  | 
Dst | Cst | Hop
A |  | –
B | 3 | B
C | 1 | C
D | 0 | D
E |  | –
F |  | –
Table for E |  | 
Dst | Cst | Hop
A | 2 | A
B |  | –
C |  | –
D |  | –
E | 0 | E
F | 3 | F
Table for F |  | 
Dst | Cst | Hop
A | 6 | A
B | 1 | B
C | 1 | C
D |  | –
E | 3 | E
F | 0 | F
Optimum 1-hop paths

## Slide 140: Iteration #1
Table for A |  | 
Dst | Cst | Hop
A | 0 | A
B | 4 | B
C | 7 | F
D | 7 | B
E | 2 | E
F | 5 | E
Table for B |  | 
Dst | Cst | Hop
A | 4 | A
B | 0 | B
C | 2 | F
D | 3 | D
E | 4 | F
F | 1 | F
Table for C |  | 
Dst | Cst | Hop
A | 7 | F
B | 2 | F
C | 0 | C
D | 1 | D
E | 4 | F
F | 1 | F
Table for D |  | 
Dst | Cst | Hop
A | 7 | B
B | 3 | B
C | 1 | C
D | 0 | D
E |  | –
F | 2 | C
Table for E |  | 
Dst | Cst | Hop
A | 2 | A
B | 4 | F
C | 4 | F
D |  | –
E | 0 | E
F | 3 | F
Table for F |  | 
Dst | Cst | Hop
A | 5 | B
B | 1 | B
C | 1 | C
D | 2 | C
E | 3 | E
F | 0 | F
Optimum 2-hop paths
A
E
F
C
D
B
2
3
6
4
1
1
1
3

## Slide 141: Iteration #2
Table for A |  | 
Dst | Cst | Hop
A | 0 | A
B | 4 | B
C | 6 | E
D | 7 | B
E | 2 | E
F | 5 | E
Table for B |  | 
Dst | Cst | Hop
A | 4 | A
B | 0 | B
C | 2 | F
D | 3 | D
E | 4 | F
F | 1 | F
Table for C |  | 
Dst | Cst | Hop
A | 6 | F
B | 2 | F
C | 0 | C
D | 1 | D
E | 4 | F
F | 1 | F
Table for D |  | 
Dst | Cst | Hop
A | 7 | B
B | 3 | B
C | 1 | C
D | 0 | D
E | 5 | C
F | 2 | C
Table for E |  | 
Dst | Cst | Hop
A | 2 | A
B | 4 | F
C | 4 | F
D | 5 | F
E | 0 | E
F | 3 | F
Table for F |  | 
Dst | Cst | Hop
A | 5 | B
B | 1 | B
C | 1 | C
D | 2 | C
E | 3 | E
F | 0 | F
Optimum 3-hop paths
A
E
F
C
D
B
2
3
6
4
1
1
1
3

## Slide 142: Distance Vector: Link Cost Changes
Link cost changes:
Node detects local link cost change
Updates distance table
If cost change in least cost path, notify neighbors
X
Z
1
4
50
Y
1
algorithm
terminates
“good
news
travels
fast”

## Slide 143: Distance Vector: Link Cost Changes
Link cost changes:
Good news travels fast
Bad news travels slow - “count to infinity” problem!
X
Z
1
4
50
Y
60
algorithm
continues
on!

## Slide 144: Distance Vector: Split Horizon
If Z routes through Y to get to X :
Z does not advertise its route to X back to Y
algorithm
terminates
X
Z
1
4
50
Y
60
?
?
?

## Slide 145: Distance Vector: Poison Reverse
If Z routes through Y to get to X :
Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
Immediate notification of unreachability, rather than split horizon timeout waiting for advertisement
Will this completely solve count to infinity problem?
X
Z
1
4
50
Y
60
algorithm
terminates

## Slide 146: Comparison of LS and DV algorithms
message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
  convergence time varies
speed of convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network

## Slide 147
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 148: Intra-AS Routing
also known as interior gateway protocols (IGP)
most common intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary)

## Slide 149: Interior Gateway Protocols (IGP)
most common Intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary)
IGP
EGP

## Slide 150: RIP ( Routing Information Protocol)
included in BSD-UNIX distribution in 1982
distance vector algorithm
  distance metric: # hops (max = 15 hops), each link has cost 1
  DVs exchanged with neighbors every 30 sec in response message (aka advertisement)
  each advertisement: list of up to 25 destination subnets (in IP addressing sense)
D
C
B
A
u
v
w
x
y
z
subnet hops
u 1
v 2
w 2
x 3
y 3
z 2
from router A to destination subnets:

## Slide 151: RIP: example
destination subnet next router # hops to dest
w A 2
y B 2
z B 7
x -- 1
…. …. ....
routing table in router D
w
x
y
z
A
C
D
B

## Slide 152: RIP: example
w
x
y
z
A
C
D
B
destination subnet next router # hops to dest
w A 2
y B 2
z B 7
x -- 1
…. …. ....
routing table in router D
A
5
dest next hops
w - 1
x - 1
z C 4
…. … ...
A-to-D advertisement

## Slide 153: RIP table processing
RIP routing tables managed by application-level process called route-d (daemon)
advertisements sent in UDP packets, periodically repeated
physical
link
network forwarding
(IP) table
transport
(UDP)
routed
physical
link
network
(IP)
transprt
(UDP)
routed
forwarding
table

## Slide 155: RIP Updates
Initial
  When router first starts, asks for copy of table for every neighbor
  Uses it to iteratively generate own table
Periodic
  Every 30 seconds, router sends copy of its table to each neighbor
  Neighbors use it to iteratively update their tables
Triggered
  When every entry changes, send copy of entry to neighbors
    Except for one causing update (split horizon rule)
  Neighbors use it to update their tables

## Slide 156: RIP Staleness / Oscillation Control
Small Infinity
  Count to infinity doesn’t take very long
Route Timer
  Every route has timeout limit of 180 seconds
    Reached when haven’t received update from next hop for 6 periods
  If not updated, set to infinity
  Soft-state refresh  important concept!
Behavior
  When router or link fails, can take minutes to stabilize
Notes:   Lots of subtlety to get good implementation (RFC 1058).

## Slide 157: OSPF (Open Shortest Path First)
“open”: publicly available
uses link state algorithm
  LS packet dissemination
  topology map at each node
  route computation using Dijkstra’s algorithm
OSPF advertisement carries one entry per neighbor
advertisements flooded to entire AS
  carried in OSPF messages directly over IP (rather than TCP or UDP
IS-IS routing protocol: nearly identical to OSPF

## Slide 158: OSPF “advanced” features (not in RIP)
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
for each link, multiple cost metrics for different TOS (e.g., satellite link cost set “low” for best effort ToS; high for real time ToS)
integrated uni- and multicast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.

## Slide 159: Hierarchical OSPF
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers

## Slide 160: OSPF Reliable Flooding

## Slide 161: OSPF Flooding Operation
Node X Receives LSA from Node Y
  With Sequence Number q
  Looks for entry with same origin/link ID
Cases
  No entry present
    Add entry, propagate to all neighbors other than Y
  Entry present with sequence number p < q
    Update entry, propagate to all neighbors other than Y
  Entry present with sequence number p > q
    Send entry back to Y
    To tell Y that it has out-of-date information
  Entry present with sequence number p = q
    Ignore it

## Slide 162: Flooding Issues
When should it be performed
  Periodically
  When status of link changes
    Detected by connected node
What happens when router goes down & back up
  Sequence number reset to 0
    Other routers may have entries with higher sequence numbers
  Router will send out LSAs with number 0
  Will get back LSAs with last valid sequence number p
  Router sets sequence number to p+1 & resends

## Slide 163: OSPF Hello Packet
Notes: תרגיל מתוך הבחינות

## Slide 164
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 165: Hierarchical routing
scale: with 600 million destinations:
can’t store all dest’s in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
our routing study thus far - idealization
all routers identical
network “flat”
… not true in practice

## Slide 166: Hierarchical routing
aggregate routers into regions, “autonomous systems” (AS)
routers in same AS run same routing protocol
  “intra-AS” routing protocol
  routers in different AS can run different intra-AS routing protocol
gateway router:
at “edge” of its own AS
has link to router in another AS

## Slide 167: Areas
Divide network into areas
  Areas can have nested sub-areas
Hierarchically address nodes in a network
  Sequentially number top-level areas
  Sub-areas of area are labeled relative to that area
  Nodes are numbered relative to the smallest containing area

## Slide 168: Area Hierarchy Addressing
1
2
3
1.1
1.2
2.1
2.2
3.1
3.2
2.2.1
2.2.2
1.2.1
1.2.2

## Slide 169: Interconnected ASes
forwarding table configured by both intra- and inter-AS routing algorithm
  intra-AS sets entries for internal dests
  inter-AS & intra-AS sets entries for external dests
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c

## Slide 170: Inter-AS tasks
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
job of inter-AS routing!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

## Slide 171: Example: setting forwarding table in router 1d
suppose AS1 learns (via inter-AS protocol) that subnet x reachable via AS3 (gateway 1c), but not via AS2
  inter-AS protocol propagates reachability info to all internal routers
router 1d determines from intra-AS routing info that its interface I is on the least cost path to 1c
  installs forwarding table entry (x,I)
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
x
…

## Slide 172: Example: choosing among multiple ASes
now suppose AS1 learns from inter-AS protocol that subnet x is reachable from AS3 and from AS2.
to configure forwarding table, router 1d must determine which gateway it should forward packets towards for dest x
  this is also job of inter-AS routing protocol!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
x
……
…
?

## Slide 173: Example: choosing among multiple ASes
now suppose AS1 learns from inter-AS protocol that subnet x is reachable from AS3 and from AS2.
to configure forwarding table, router 1d must determine towards which gateway it should forward packets for dest x
  this is also job of inter-AS routing protocol!
hot potato routing: send packet towards closest of two routers.
learn from inter-AS
protocol that subnet
x is reachable via
multiple gateways
use routing info
from intra-AS
protocol to determine
costs of least-cost
paths to each
of the gateways
hot potato routing:
choose the gateway
that has the
smallest least cost
determine from
forwarding table the
interface I that leads
to least-cost gateway.
Enter (x,I) in
forwarding table

## Slide 175: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASs.
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy.
allows subnet to advertise its existence to rest of Internet: “I am here”

## Slide 176: BGP basics
when AS3 advertises a prefix to AS1:
  AS3 promises it will forward datagrams towards that prefix
  AS3 can aggregate prefixes in its advertisement
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
BGP session: two BGP routers (“peers”) exchange BGP messages:
  advertising paths to different destination network prefixes (“path vector” protocol)
  exchanged over semi-permanent TCP connections
BGP
message
Notes: אוניברסיטה מסלול בוקר

## Slide 177: BGP basics: distributing path information
using eBGP session between 3a and 1c, AS3 sends prefix reachability info to AS1.
  1c can then use iBGP do distribute new prefix info to all routers in AS1
  1b can then re-advertise new reachability info to AS2 over 1b-to-2a eBGP session
when router learns of new prefix, it creates entry for prefix in its forwarding table.
AS3
AS2
3b
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
eBGP session
iBGP session

## Slide 178: Path attributes and BGP routes
advertised prefix includes BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: contains ASs through which prefix advertisement has passed: e.g., AS 67, AS 17
  NEXT-HOP: indicates specific internal-AS router to next-hop AS. (may be multiple links from current AS to next-hop-AS)
gateway router receiving route advertisement uses import policy to accept/decline
  e.g., never route through AS x
  policy-based routing

## Slide 179: BGP route selection
router may learn about more than 1 route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 180: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to peer and authenticates sender
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 181: BGP routing policy
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
  X does not want to route from B via X to C
  .. so X will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 182: BGP routing policy (2)
A advertises path AW to B
B advertises path BAW to X
Should B advertise path BAW to C?
  No way! B gets no “revenue” for routing CBAW since neither W nor C are B’s customers
  B wants to force C to route to w via A
  B wants to route only to/from its customers!
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 183: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its net.
intra-AS: single admin, so no policy decisions needed
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy may dominate over performance

## Slide 184: BGP Operations (Simplified)
Establish session on
TCP port 179
Exchange all
active routes
Exchange incremental
updates
AS1
AS2
While connection
is ALIVE exchange
route UPDATE messages
BGP session

## Slide 185: Two Types of BGP Neighbor Relationships
External Neighbor (eBGP) in a different Autonomous Systems
Internal Neighbor (iBGP) in the same Autonomous System
AS1
AS2
eBGP
iBGP
iBGP is routed (using IGP!)

## Slide 186: AS-Path Attribute
Sequence of ASes a route has traversed
Loop detection
  Discard updates containing your own AS number
Apply policy
AS 100
AS 300
AS 200
AS 500
AS 400
170.10.0.0/16
180.10.0.0/16
150.10.0.0/16
Network Path
180.10.0.0/16 300 200 100
170.10.0.0/16 300 200
150.10.0.0/16 300 400
Network Path
180.10.0.0/16 300 200 100
170.10.0.0/16 300 200

## Slide 187: Customers Don’t Always Need BGP
provider
customer
Default route 0.0.0.0/0
pointing to provider.
Configured route 192.0.2.0/24
pointing to customer
192.0.2.0/24
Static routing is the most common way of connecting an
autonomous routing domain to the Internet.
So many net-admin don’t use/know BGP …

## Slide 188: Customer-Provider Hierarchy
IP traffic
provider
customer

## Slide 189: סרטון של כותבי הסרט
Notes: https://media.pearsoncmg.com/aw/ecs_kurose_compnetwork_7/cw/videonotes-cw.php

## Slide 190: לינקים חשובים
https://www.youtube.com/watch?v=z8INzy9E628 – להראות בכיתה
https://www.youtube.com/watch?v=ZTJIkjgyuZE&app=desktop